## Slide 1
Linear programming and duality
2105623 Optimization of Chemical
Processes
26 October 2026 · 180-minute class
Geometry, Simplex, optimality
certificates, and resource values
2105623 · Linear programming and duality
01

## Slide 2
Plan for the three-hour class
2105623 · Linear programming and duality
02
Minutes | Topic
0–23 | LP geometry and corner solutions
23–56 | Basic feasible solutions and Simplex
56–66 | Break
66–103 | Duality and complementary slackness
103–163 | Sensitivity, solver output, capacity decisions
163–180 | Exit ticket, solutions, and connected recap

## Slide 3
What makes a model linear?
max cᵀx subject to Ax ≤ b, x ≥ 0
Coefficients are fixed; decision variables are continuous.
x + 2y is linear. xy and x² are not.
A binary restriction changes an LP into a MILP.
2105623 · Linear programming and duality
03

## Slide 4
Running example: two production routes
x, y = tonnes/day; contribution = $100/day units.
Choose continuous production; no fixed startup cost.
2105623 · Linear programming and duality
04
Item | Route x | Route y | Daily limit
Resource 1 | 1 unit/t | 1 unit/t | 4 units/day
Resource 2 | 2 units/t | 1 unit/t | 5 units/day
Contribution | 3 × $100/t | 2 × $100/t | Maximize

## Slide 5
The production LP
max z = 3x + 2y
x + y ≤ 4
2x + y ≤ 5
x ≥ 0, y ≥ 0
2105623 · Linear programming and duality
05

## Slide 6
Objective contours and the best feasible point
3x + 2y = z gives parallel lines.
Move the line toward larger z.
The last contact is (x*, y*) = (1, 3).
z* = 9, or $900/day.
2105623 · Linear programming and duality
06

## Slide 7
Why compare extreme points?
On a nonempty bounded polytope, a linear objective has an optimal extreme point.
A convex combination cannot beat all vertices used in that combination.
2105623 · Linear programming and duality
07
Vertex (x, y) | z = 3x + 2y
(0, 0) | 0
(2.5, 0) | 7.5
(1, 3) | 9
(0, 4) | 8

## Slide 8
An LP can have many optimal solutions
Change only the objective to max x
+ y.
Every point from (0,4) to (1,3) is
optimal.
The entire optimal edge has value 4.
2105623 · Linear programming and duality
08

## Slide 9
Infeasible and unbounded are different
Infeasible: x ≤ 1 and x ≥ 2 cannot
both hold.
Unbounded: max x with only x ≥ 0
has no finite maximum.
2105623 · Linear programming and duality
09

## Slide 10
Quick check: feasibility before profit
Original LP: max 3x+2y; x+y≤4, 2x+y≤5, x,y≥0.
A: (2,2) gives z=10. B: (1,3) gives z=9.
Which point can be accepted? Explain the failed constraint.
2105623 · Linear programming and duality
10

## Slide 11
Slack variables and standard form
x + y + s₁ = 4
2x + y + s₂ = 5
x, y, s₁, s₂ ≥ 0
s₁ and s₂ measure unused resources.
Shown: (x,y)=(2.5,0), so (s₁,s₂)=(1.5,0).
2105623 · Linear programming and duality
11

## Slide 12
A basis selects the variables we solve for
Choose two independent columns as a basis for the two equations.
Set the other two variables to zero, then solve.
A basic solution is feasible only if every variable is nonnegative.
2105623 · Linear programming and duality
12
Basis | Nonbasic variables | Basic solution
{s₁, s₂} | x=y=0 | s₁=4, s₂=5
{x, s₁} | y=s₂=0 | x=2.5, s₁=1.5
{x, y} | s₁=s₂=0 | x=1, y=3

## Slide 13
The Simplex decision at each step
1. Choose an improving nonbasic
variable.
2. Increase it until a basic variable
reaches zero.
3. Pivot: exchange the entering and
leaving variables.
Positive reduced cost improves z if a
positive feasible step exists.
2105623 · Linear programming and duality
13

## Slide 14
Pivot 1: x enters, s₂ leaves
At the origin: z = 3x + 2y. Choose x.
With y=0: s₁=4−x; s₂=5−2x.
Ratio test: 4/1=4; 5/2=2.5.
Move to (2.5,0); z=7.5.
2105623 · Linear programming and duality
14

## Slide 15
Dictionary after the first pivot
x = 2.5 − 0.5y − 0.5s₂
s₁ = 1.5 − 0.5y + 0.5s₂
z = 7.5 + 0.5y − 1.5s₂
Nonbasic: y=s₂=0. The +0.5 coefficient means y can improve z.
2105623 · Linear programming and duality
15

## Slide 16
Pivot 2: y enters, s₁ leaves
Hold s₂=0 and increase y.
x≥0 gives y≤2.5/0.5=5.
s₁≥0 gives y≤1.5/0.5=3.
Thus y=3, x=1, s₁=s₂=0; z=9.
2105623 · Linear programming and duality
16

## Slide 17
The final dictionary certifies optimality
x = 1 + s₁ − s₂
y = 3 − 2s₁ + s₂
z = 9 − s₁ − s₂
Because s₁,s₂≥0, every feasible point satisfies z≤9.
2105623 · Linear programming and duality
17

## Slide 18
Degeneracy and starting feasibility
A degenerate BFS has at least one
zero basic variable.
A pivot may change the basis
without improving the point.
At b=(4,8), the basis {x,y} gives
x=4, y=0.
If a feasible slack basis is
unavailable, use Phase I or another
initialization.
2105623 · Linear programming and duality
18

## Slide 19
Practice: change the contribution
Keep x+y≤4, 2x+y≤5, x,y≥0.
Change the objective to max z=x+3y.
Choose the first entering variable and apply the ratio test.
Predict the optimum and write a stopping argument.
2105623 · Linear programming and duality
19

## Slide 20
Practice solution: one pivot is enough
y enters; min(4/1,5/1)=4, so s₁
leaves.
y=4−x−s₁; s₂=1−x+s₁.
z=x+3y=12−2x−3s₁≤12.
Optimal: (x,y)=(0,4), slack=(0,1),
z*=12.
2105623 · Linear programming and duality
20

## Slide 21
Break
10 minutes
After the break: what is one more unit of a resource worth?
2105623 · Linear programming and duality
21

## Slide 22
The dual prices the resources
Return to max z=3x+2y, b=(4,5).
u, v price resources 1 and 2
($100/unit).
A tonne of x uses resources worth
u+2v.
A tonne of y uses resources worth u+v.
Cover contributions: u+2v≥3, u+v≥2.
2105623 · Linear programming and duality
22

## Slide 23
Primal and dual side by side
Primal: max cᵀx, subject to Ax≤b, x≥0.
Dual: min bᵀu, subject to Aᵀu≥c, u≥0.
Here: min w=4u+5v
subject to u+2v≥3, u+v≥2, u,v≥0.
2105623 · Linear programming and duality
23

## Slide 24
Signs depend on the formulation
For a maximization primal:
2105623 · Linear programming and duality
24
Primal feature | Dual counterpart
Constraint aᵢᵀx ≤ bᵢ | uᵢ ≥ 0
Constraint aᵢᵀx ≥ bᵢ | uᵢ ≤ 0
Constraint aᵢᵀx = bᵢ | uᵢ is free
Variable xⱼ ≥ 0 | (Aᵀu)ⱼ ≥ cⱼ
Variable xⱼ ≤ 0 | (Aᵀu)ⱼ ≤ cⱼ
Variable xⱼ is free | (Aᵀu)ⱼ = cⱼ

## Slide 25
Weak duality gives an upper bound
For any primal-feasible x and dual-feasible u:
cᵀx ≤ xᵀAᵀu = uᵀAx ≤ uᵀb.
Example: (u,v)=(2,1) is feasible; w=13.
Therefore every feasible production plan has z≤13.
2105623 · Linear programming and duality
25

## Slide 26
Dual geometry: tighten the upper bound
The dual feasible set lies above both
price lines.
Minimize 4u+5v over that set.
Candidate corner prices: (3,0), (1,1),
(0,2).
Their bounds are 12, 9, and 10.
2105623 · Linear programming and duality
26

## Slide 27
Solve the dual and compare
u+2v=3 and u+v=2 → u=v=1.
Dual value: 4(1)+5(1)=9.
Primal point (1,3) is feasible and
gives 9.
Feasible values meet: both solutions
are optimal.
2105623 · Linear programming and duality
27

## Slide 28
Strong duality for linear programs
If an LP is feasible with a finite optimum, its dual also has an optimum with
the same value.
A primal unbounded above implies the dual is infeasible.
Primal infeasible does not by itself imply dual unbounded.
2105623 · Linear programming and duality
28

## Slide 29
The duality gap separates two kinds of waste
s=b−Ax≥0; r=Aᵀu−c≥0.
w−z = uᵀs + xᵀr ≥ 0.
Unused priced resources contribute uᵀs.
Producing below the assigned resource cost contributes xᵀr.
2105623 · Linear programming and duality
29

## Slide 30
Complementary slackness
For primal-feasible x and dual-feasible u:
uᵢ(bᵢ−aᵢᵀx)=0 for each resource.
xⱼ((Aᵀu)ⱼ−cⱼ)=0 for each product.
Unused resource implies zero price. Positive output implies a tight dual
constraint.
A binding resource can have zero price.
2105623 · Linear programming and duality
30

## Slide 31
LP duality is KKT in a special form
Rewrite max cᵀx as min −cᵀx.
L = −cᵀx + uᵀ(Ax−b) − rᵀx.
Stationarity: −c + Aᵀu − r = 0.
Primal feasibility, u,r≥0, and complementarity complete the optimality
conditions.
2105623 · Linear programming and duality
31

## Slide 32
Practice: a dual certificate
For max x+3y with the same two resource constraints:
1. Write the dual.
2. Test primal (0,4) and dual (u,v)=(3,0).
3. Check both objectives and all complementarity products.
2105623 · Linear programming and duality
32

## Slide 33
Practice solution: zero price for unused capacity
Dual: min 4u+5v; u+2v≥1, u+v≥3; u,v≥0.
At (3,0): w=12=z(0,4).
Resource slack: (0,1). Dual slack: (2,0).
Products: 3·0=0, 0·1=0, 0·2=0, 4·0=0.
2105623 · Linear programming and duality
33

## Slide 34
Shadow prices: value per extra unit
Return to c=(3,2), b=(4,5): u*=v*=1.
Hold A and c fixed; keep the same basis feasible and optimal.
Then Δz* = u*Δb₁ + v*Δb₂ exactly.
Each additional resource unit is worth $100 within this region.
2105623 · Linear programming and duality
34

## Slide 35
1. Resource 1 changes, resource 2 stays fixed
Maximize z = 3x + 2y.
x + y ≤ b₁, 2x + y ≤ 5, x,y ≥ 0.
At b₁ = 4: (x,y) = (1,3), z* = 9.
How far can we change b₁ and keep its
shadow price equal to 1?
2105623 · Linear programming and duality
35

## Slide 36
2. The intersection moves with b₁
Suppose both resources remain fully
used.
x + y = b₁
2x + y = 5
Subtract the equations: x = 5 − b₁.
Substitute back: y = 2b₁ − 5.
2105623 · Linear programming and duality
36

## Slide 37
3. Nonnegativity gives the allowable range
x = 5 − b₁ ≥ 0 requires b₁ ≤ 5.
y = 2b₁ − 5 ≥ 0 requires b₁ ≥ 2.5.
Together: 2.5 ≤ b₁ ≤ 5.
At 2.5: (x,y) = (2.5,0).
At 5: (x,y) = (0,5).
2105623 · Linear programming and duality
37

## Slide 38
4. Inside the range: b₁ = 4.5
x = 5 − 4.5 = 0.5.
y = 2(4.5) − 5 = 4.
z* = 3(0.5) + 2(4) = 9.5.
From b₁ = 4: Δb₁ = 0.5, Δz* = 0.5.
The extra contribution is $50.
2105623 · Linear programming and duality
38

## Slide 39
5. Duality confirms the shadow price
At the intersection: z* = 3(5−b₁) +
2(2b₁−5) = b₁ + 5.
Dual prices (u,v) = (1,1) remain
feasible.
Dual value: w = b₁u + 5v = b₁ + 5.
Primal value = dual value, so both are
optimal.
Within the range: Δz* = 1 × Δb₁.
2105623 · Linear programming and duality
39

## Slide 40
6. Below the range: b₁ = 2
The old intersection is (3,−1), which is
infeasible.
The optimum is (x,y) = (2,0), z* = 6.
Resource 2 has slack: 5 − 2(2) = 1.
For 0 < b₁ < 2.5: z* = 3b₁.
Shadow price of resource 1: 3.
2105623 · Linear programming and duality
40

## Slide 41
7. Above the range: b₁ = 6
The old intersection is (−1,7), which is
infeasible.
The optimum is (x,y) = (0,5), z* = 10.
Resource 1 has slack: 6 − 5 = 1.
For b₁ > 5: z* = 10.
Shadow price of resource 1: 0.
2105623 · Linear programming and duality
41

## Slide 42
8. The value function changes slope
0 ≤ b₁ ≤ 2.5: z* = 3b₁.
2.5 ≤ b₁ ≤ 5: z* = b₁ + 5.
b₁ ≥ 5: z* = 10.
The middle formula includes both
endpoints.
At 2.5 and 5, left and right slopes
differ.
2105623 · Linear programming and duality
42

## Slide 43
1. Resource 2 changes, resource 1 stays fixed
Maximize z = 3x + 2y.
x + y ≤ 4, 2x + y ≤ b₂, x,y ≥ 0.
At b₂ = 5: (x,y) = (1,3), z* = 9.
How far can b₂ change while its shadow
price stays at 1?
2105623 · Linear programming and duality
43

## Slide 44
2. The intersection as a function of b₂
Suppose both resources remain fully
used.
x + y = 4
2x + y = b₂
Subtract the equations: x = b₂ − 4.
Substitute back: y = 8 − b₂.
2105623 · Linear programming and duality
44

## Slide 45
3. Nonnegativity gives 4 ≤ b₂ ≤ 8
x = b₂ − 4 ≥ 0 requires b₂ ≥ 4.
y = 8 − b₂ ≥ 0 requires b₂ ≤ 8.
Together: 4 ≤ b₂ ≤ 8.
At 4: (x,y) = (0,4). At 8: (x,y) = (4,0).
From b₂ = 5: decrease by 1 or increase
by 3.
2105623 · Linear programming and duality
45

## Slide 46
4. Inside the range: b₂ = 6
x = 6 − 4 = 2.
y = 8 − 6 = 2.
z* = 3(2) + 2(2) = 10.
From b₂ = 5: Δb₂ = 1, Δz* = 1.
The extra contribution is $100.
2105623 · Linear programming and duality
46

## Slide 47
5. Duality confirms the price of resource 2
At the intersection: z* = 3(b₂−4) +
2(8−b₂) = b₂ + 4.
Dual prices (u,v) = (1,1) remain
feasible.
Dual value: w = 4u + b₂v = b₂ + 4.
Primal value = dual value, so both are
optimal.
Within the range: Δz* = 1 × Δb₂.
2105623 · Linear programming and duality
47

## Slide 48
6. Below the range: b₂ = 3
The intersection formula gives (−1,5),
which is infeasible.
The optimum is (x,y) = (0,3), z* = 6.
Resource 1 has slack: 4 − 3 = 1.
For 0 < b₂ < 4: z* = 2b₂.
Shadow price of resource 2: 2.
2105623 · Linear programming and duality
48

## Slide 49
7. Above the range: b₂ = 9
The intersection formula gives (5,−1),
which is infeasible.
The optimum is (x,y) = (4,0), z* = 12.
Resource 2 has slack: 9 − 2(4) = 1.
For b₂ > 8: z* = 12.
Shadow price of resource 2: 0.
2105623 · Linear programming and duality
49

## Slide 50
8. The value function for resource 2
0 ≤ b₂ ≤ 4: z* = 2b₂.
4 ≤ b₂ ≤ 8: z* = b₂ + 4.
b₂ ≥ 8: z* = 12.
At 4: left slope 2, right slope 1.
At 8: left slope 1, right slope 0.
2105623 · Linear programming and duality
50

## Slide 51
9. Changing both resources needs a joint check
With both RHS values changing:
x = b₂ − b₁, y = 2b₁ − b₂.
The same basis requires b₁ ≤ b₂ ≤ 2b₁.
(b₁,b₂) = (5,4) is outside this region.
Its true optimum is (x,y)=(0,4), z*=8.
2105623 · Linear programming and duality
51

## Slide 52
1. Objective sensitivity keeps the feasible set fixed
Maximize z = c₁x + 2y.
x + y ≤ 4, 2x + y ≤ 5, x,y ≥ 0.
Baseline c₁ = 3: (x,y) = (1,3), z* = 9.
Only the contribution from product x
changes.
Which c₁ values keep (1,3) optimal?
2105623 · Linear programming and duality
52

## Slide 53
2. Complementary slackness determines the prices
At (1,3), both products have positive
output.
Their dual constraints must be tight:
u + 2v = c₁, u + v = c₂.
Subtract: v = c₁ − c₂.
Then u = 2c₂ − c₁.
2105623 · Linear programming and duality
53

## Slide 54
3. Nonnegative dual prices give the range
u = 2c₂ − c₁ ≥ 0 requires c₁ ≤ 2c₂.
v = c₁ − c₂ ≥ 0 requires c₁ ≥ c₂.
Together: c₂ ≤ c₁ ≤ 2c₂.
With c₂ = 2: 2 ≤ c₁ ≤ 4.
The contour slope −c₁/2 lies between
−2 and −1.
2105623 · Linear programming and duality
54

## Slide 55
4. Below the range: c₁ = 1
Maximize z = x + 2y.
At (1,3): z = 7.
The optimum is (0,4), with z* = 8.
The old price formula gives v = −1.
For c₁ < 2: (0,4) stays optimal.
2105623 · Linear programming and duality
55

## Slide 56
5. At c₁ = 2, an entire edge is optimal
z = 2x + 2y = 2(x+y) ≤ 8.
Every feasible point on x+y=4 attains
8.
The optimal edge runs from (0,4) to
(1,3).
(1,3) is still optimal, but not unique.
Dual prices: (u,v) = (2,0).
2105623 · Linear programming and duality
56

## Slide 57
6. Inside the range: c₁ = 3.5
The optimum stays at (x,y) = (1,3).
z* = 3.5(1) + 2(3) = 9.5.
u = 4 − 3.5 = 0.5, v = 3.5 − 2 = 1.5.
Dual value: 4u + 5v = 9.5.
The production plan stays fixed, but
resource prices change.
2105623 · Linear programming and duality
57

## Slide 58
7. At c₁ = 4, the other edge is optimal
z = 4x + 2y = 2(2x+y) ≤ 10.
Every feasible point on 2x+y=5 attains
10.
The optimal edge runs from (1,3) to
(2.5,0).
(1,3) remains one of the optimal
solutions.
Dual prices: (u,v) = (0,2).
2105623 · Linear programming and duality
58

## Slide 59
8. Above the range: c₁ = 5
Maximize z = 5x + 2y.
At (1,3): z = 11.
The optimum is (2.5,0), with z* = 12.5.
The old price formula gives u = −1.
For c₁ > 4: (2.5,0) stays optimal.
2105623 · Linear programming and duality
59

## Slide 60
9. Optimal value as the coefficient changes
c₁ < 2: z* = 8, with unique x* = 0.
2 ≤ c₁ ≤ 4: z* = c₁ + 6.
c₁ > 4: z* = 2.5c₁, with unique x* =
2.5.
On open intervals, dz*/dc₁ = x*.
At 2: x* ∈ [0,1]; at 4: x* ∈ [1,2.5].
2105623 · Linear programming and duality
60

## Slide 61
1. Return to the original production model
Maximize z = 3x + 2y.
x + y ≤ 4; 2x + y ≤ 5; x,y ≥ 0.
Baseline: (x,y) = (1,3), z* = 9.
Resource prices: u = 1, v = 1.
Could a new product improve this plan?
2105623 · Linear programming and duality
61

## Slide 62
2. Price the resources used by the new product
New product t: contribution cₜ = 4.
Each unit uses resource 1: 1; resource
2: 2.
At the old prices, resource value = 1u
+ 2v = 3.
Contribution 4 exceeds resource value
3 by 1.
2105623 · Linear programming and duality
62

## Slide 63
3. Derive reduced cost from a feasible exchange
Keep both resources fully used:
x + y + t = 4; 2x + y + 2t = 5.
Subtract: x + t = 1, so x = 1 − t and y
= 3.
z = 3(1−t) + 2(3) + 4t = 9 + t.
Thus c̄ₜ = cₜ − (u+2v) = 4 − 3 = 1.
2105623 · Linear programming and duality
63

## Slide 64
4. The feasible step ends when x reaches zero
x = 1 − t ≥ 0 and t ≥ 0 require 0 ≤ t ≤
1.
At t = 1: (x,y,t) = (0,3,1), z = 10.
At t = 1.5, the same rule gives x =
−0.5.
So z = 9 + t cannot be extrapolated
past t = 1.
The basis must change when x leaves.
2105623 · Linear programming and duality
64

## Slide 65
5. The new product invalidates the old certificate
Max 3x + 2y + 4t; x,y,t ≥ 0.
x+y+t ≤ 4; 2x+y+2t ≤ 5.
Dual: u,v ≥ 0; u+2v ≥ 3; u+v ≥ 2;
u+2v ≥ 4.
Old prices (1,1) fail: 3 < 4 for t.
So the old upper bound 9 is invalid.
2105623 · Linear programming and duality
65

## Slide 66
6. Reoptimize and certify the new maximum
Choose new dual prices (u,v) = (0,2).
Resource values: x → 4 ≥ 3; y → 2; t →
4.
Every feasible plan has z ≤ 4u + 5v =
10.
Plan (0,3,1) attains 10, so it is optimal.
New reduced costs (x,y,t) = (−1,0,0).
2105623 · Linear programming and duality
66

## Slide 67
7. More than one new production plan is optimal
With x = 0: y+t ≤ 4 and y+2t ≤ 5.
On y+2t = 5, profit 2y+4t = 10.
Feasibility gives 1 ≤ t ≤ 2.5 and y =
5−2t.
Examples: (0,3,1), (0,2,1.5), (0,0,2.5).
Beyond t=1, reallocate y; profit stays
at 10.
2105623 · Linear programming and duality
67

## Slide 68
8. Compare three possible product contributions
Keep the new column fixed at (1,2).
At old prices: c̄ₜ = cₜ − 3.
cₜ = 2: c̄ₜ = −1; optimal t = 0, z* = 9.
cₜ = 3: c̄ₜ = 0; feasible exchange keeps
z* = 9.
cₜ = 4: c̄ₜ = +1; reoptimize to z* = 10.
2105623 · Linear programming and duality
68

## Slide 69
9. A reduced-cost decision checklist
For max: c̄ⱼ = cⱼ − aⱼᵀπ, where π = (u,v).
1. Price the column at the current dual
prices.
2. Check a feasible step and its limit.
3. Reoptimize; check a new dual
certificate.
For nonbasic variables at lower bounds:
max c̄≤0; min c̄≥0 at an optimal basis.
2105623 · Linear programming and duality
69

## Slide 70
1. Send a minimization model to SciPy
Return to the original LP; no new
product t.
Max z = 3x+2y becomes min F =
−3x−2y.
c = [−3, −2]; A = [[1,1], [2,1]].
b = [4,5]; default bounds: (0,None).
linprog(c, A_ub=A, b_ub=b,
method="highs")
2105623 · Linear programming and duality
70

## Slide 71
2. Read the actual solver output
Return to the original two-product LP. SciPy minimizes −3x−2y; max-profit shadow prices =
−marginals = (1,1).
Check status, feasibility, objective, and a small RHS change.
2105623 · Linear programming and duality
71
Output | Expected value | Meaning
success | True | Optimal termination
x | [1, 3] | Production
fun | −9 | Minimized negative contribution
ineqlin.residual | [0, 0] | Unused capacity
ineqlin.marginals | [−1, −1] | Sensitivity of the minimized objective

## Slide 72
3. Derive the sign instead of memorizing it
Where F* is differentiable: mᵢ = ∂F*/∂bᵢ.
Since z*(b) = −F*(b): ∂z*/∂bᵢ = −mᵢ.
Here m = (−1,−1), so (u,v) = (1,1).
Extra capacity lowers F* and raises
profit z*.
Units: $100 of profit per extra capacity
unit.
2105623 · Linear programming and duality
72

## Slide 73
4. Verify resource 1 with a small perturbation
Change only b₁: 4 → 4.1; keep b₂ = 5.
Prediction: ΔF* = (−1)(0.1) = −0.1.
Rerun: (x,y) = (0.9,3.2), F* = −9.1.
Profit: 9 → 9.1, a gain of $10/day.
(−9.1+9)/0.1 = −1; (9.1−9)/0.1 = +1.
2105623 · Linear programming and duality
73

## Slide 74
5. Verify resource 2 independently
Reset b₁ = 4; change only b₂: 5 → 5.1.
Rerun: (x,y) = (1.1,2.9), F* = −9.1.
Resource use: 1.1+2.9=4;
2(1.1)+2.9=5.1.
ΔF*/0.1 = −1; Δz*/0.1 = +1.
Rows of ineqlin.marginals follow rows
of A_ub.
2105623 · Linear programming and duality
74

## Slide 75
6. A marginal is not a global prediction
Old prices apply for 2.5 ≤ b₁ ≤ 5
(b₂=5).
From b₁=4 to 6, the old rule predicts
z*=11.
Rerun at b₁=6: (x,y)=(0,5), z*=10.
Residuals = (1,0); marginals = (0,−2).
New profit shadow prices are (0,2).
2105623 · Linear programming and duality
75

## Slide 76
7. Row marginals and bound marginals differ
New example: max z=x+3y, with the
same constraints.
Solution: (0,4), z*=12; row
marginals=(−3,0).
lower.marginals = (2,0): this refers to
variable bounds.
Raise the lower bound of x: 0 → 0.1.
Then (x,y)=(0.1,3.9), F*: −12 → −11.8.
2105623 · Linear programming and duality
76

## Slide 77
8. Connect the bound marginal to reduced cost
For max z=x+3y, resource prices are
(u,v)=(3,0).
Product x has max reduced cost:
1−(3+2·0)=−2.
Its min lower-bound marginal is +2.
Forcing x≥0.1 loses 0.2 profit units =
$20/day.
Read status → objective → field/RHS →
sign → local check.
2105623 · Linear programming and duality
77

## Slide 78
1. Define the baseline and the purchase offer
Return to max z=3x+2y; capacities
(b₁,b₂)=(4,5).
Baseline: (x,y)=(1,3), z*=9 =
$900/day.
Let q ≥ 0 be extra resource 1 capacity
per day.
Offer A: q=0.5 costs $30/day in total.
Compare incremental contribution with
this new cost.
2105623 · Linear programming and duality
78

## Slide 79
2. Convert the shadow-price range into a purchase
limit
With b₂=5, the old basis needs 2.5 ≤ b₁
≤ 5.
Since b₁=4+q and q≥0, its purchase
range is 0≤q≤1.
Old shadow price u=1 means $100 per
capacity unit.
For 0≤q≤1: extra contribution
G(q)=$100q/day.
For q>1, reoptimize before valuing the
purchase.
2105623 · Linear programming and duality
79

## Slide 80
3. Add 0.5 capacity and calculate the gross gain
q=0.5 gives b₁=4.5, inside the
old-price range.
x=5−b₁=0.5; y=2b₁−5=4.
z*=3(0.5)+2(4)=9.5 = $950/day.
Gross incremental contribution:
$950−$900=$50/day.
Shadow-price check:
$100×0.5=$50/day.
2105623 · Linear programming and duality
80

## Slide 81
4. Subtract the purchase cost exactly once
Gross gain G=$50/day; purchase cost
C=$30/day.
Net benefit N=G−C=$20/day > 0: buy
Offer A.
Contribution after the new cost:
$950−$30=$920/day.
Compare $920 with the baseline $900.
Do not subtract existing variable costs
again.
2105623 · Linear programming and duality
81

## Slide 82
5. Buying 2 units crosses the useful range
q=2 gives b₁=6; the old rule predicts a
$200 gain.
Reoptimize: (x,y)=(0,5), z*=10 =
$1,000/day.
Actual gain: $1,000−$900=$100/day.
Resource 1 has slack 1; resource 2 is
fully used.
G(q)=$100q for 0≤q≤1; G(q)=$100 for
q≥1.
2105623 · Linear programming and duality
82

## Slide 83
6. Use a break-even price for the whole offer
For q=2, maximum useful payment is
$100/day.
If total cost C=$150/day:
N=$100−$150=−$50/day.
Reject: $1,000−$150=$850 < $900
baseline.
If C=$100/day: N=0, so the model is
indifferent.
If C<$100/day: N>0; buying improves
the baseline.
2105623 · Linear programming and duality
83

## Slide 84
7. If capacity is divisible, choose how much to buy
New pricing assumption:
C(q)=$60q/day; no fixed fee.
For 0≤q≤1: N(q)=100q−60q=40q.
For q≥1: N(q)=100−60q.
Best purchase: q*=1; net
benefit=$40/day.
The unit price is attractive only while
capacity adds value.
2105623 · Linear programming and duality
84

## Slide 85
8. Compare complete offers by net benefit
Choose at most one package; each
cost is a total daily cost.
A: q=0.5, C=$30 → G=$50,
N=$20/day.
B: q=1, C=$70 → G=$100, N=$30/day.
C: q=2, C=$90 → G=$100, N=$10/day.
Choose B: $900+$30=$930/day after
the new cost.
2105623 · Linear programming and duality
85

## Slide 86
Exit ticket 1: can an entire edge be optimal?
Work independently. Attempt all four
questions before the solutions.
For this question only: max z=2x+2y.
x+y≤4; 2x+y≤5; x,y≥0.
Identify the optimal edge and its
endpoints.
Explain why every point on it gives the
same best value.
2105623 · Linear programming and duality
86

## Slide 87
Exit ticket 2: is this a valid dual bound?
Return to the original objective: max
z=3x+2y.
Dual: min w=4u+5v; u,v≥0.
Constraints: u+2v≥3 and u+v≥2.
Test the candidate (u,v)=(1,0).
Compute w. Can it bound every
feasible primal value? Why?
2105623 · Linear programming and duality
87

## Slide 88
Exit ticket 3: construct an optimality certificate
Original LP: max z=3x+2y.
x+y≤4; 2x+y≤5; x,y≥0.
Find a feasible primal point and
feasible dual prices.
Show that their objective values are
equal.
State why this proves both are optimal.
2105623 · Linear programming and duality
88

## Slide 89
Exit ticket 4: when does the shadow price work?
Original LP: b₁=4, b₂=5; z*=9 and u=1.
Keep b₂=5 and change only b₁.
A. Predict z* at b₁=4.2 and check the
production plan.
B. Would the same rule predict
correctly at b₁=6?
Give the valid range and the actual
optimum at 6.
2105623 · Linear programming and duality
89

## Slide 90
Solution 1: combine a bound with an attainable edge
Step 1: z=2(x+y)≤8 from x+y≤4.
Step 2: attaining 8 requires y=4−x.
Step 3: 2x+(4−x)≤5 gives x≤1.
With nonnegativity: 0≤x≤1.
The edge from (0,4) to (1,3) is optimal;
z*=8.
2105623 · Linear programming and duality
90

## Slide 91
Solution 2: this dual candidate fails to give a bound
Step 1: (u,v)=(1,0) satisfies
nonnegativity.
Step 2: u+2v=1<3 and u+v=1<2.
So the candidate is dual infeasible.
Step 3: w=4(1)+5(0)=4 is not a valid
upper bound.
Counterexample: feasible (x,y)=(1,3)
gives z=9>4.
2105623 · Linear programming and duality
91

## Slide 92
Solution 3: verify both sides before equating values
Primal (x,y)=(1,3): resource use (4,5);
x,y≥0.
Dual (u,v)=(1,1): u+2v=3; u+v=2;
u,v≥0.
Primal value: z=3(1)+2(3)=9.
Dual value: w=4(1)+5(1)=9.
Weak duality gives z≤z*≤w. Hence
z*=9.
2105623 · Linear programming and duality
92

## Slide 93
Solution 4A: predict, then check at b₁=4.2
Step 1: 2.5≤4.2≤5, so the old shadow
price applies.
Step 2: Δb₁=0.2; z*=9+1(0.2)=9.2.
Step 3: x=5−4.2=0.8;
y=2(4.2)−5=3.4.
Check: x+y=4.2 and 2x+y=5.
Direct value: 3(0.8)+2(3.4)=9.2 =
$920/day.
2105623 · Linear programming and duality
93

## Slide 94
Solution 4B: expose the failed extrapolation at 6
Old rule predicts z=9+1(6−4)=11.
But its basis gives x=5−6=−1, y=7:
infeasible.
Actual optimum: (x,y)=(0,5), z*=10.
Dual (u,v)=(0,2) is feasible and gives
w=6(0)+5(2)=10.
Thus 10 is certified; the old price
cannot cross b₁=5.
2105623 · Linear programming and duality
94

## Slide 95
The big picture: one LP, four connected ideas
2105623 · Linear programming and duality
95

## Slide 96
1. Primal proposes a plan; dual certifies its value
Primal: max 3x+2y; x+y≤4, 2x+y≤5;
x,y≥0.
Dual: min 4u+5v; u+2v≥3, u+v≥2;
u,v≥0.
Feasible plan (1,3) gives z=9.
Feasible prices (1,1) give w=9.
Weak duality: z≤z*≤w. Equality
certifies optimality.
2105623 · Linear programming and duality
96

## Slide 97
2. Complementary slackness closes the duality gap
s₁=4−x−y; s₂=5−2x−y.
r_x=u+2v−3; r_y=u+v−2.
w−z = u·s₁ + v·s₂ + x·r_x + y·r_y.
For feasible primal and dual points, all
terms are nonnegative.
At optimum each product is zero:
u·s₁=v·s₂=x·r_x=y·r_y=0.
2105623 · Linear programming and duality
97

## Slide 98
3. Dual prices become local resource values
At capacities (4,5): (u,v)=(1,1).
Within the current basis region:
Δz*=uΔb₁+vΔb₂.
One RHS at a time: 2.5≤b₁≤5; 4≤b₂≤8.
Example: b₁=4.2, b₂=5 gives Δz*=0.2.
This is $20/day of gross gain, before
any purchase cost.
2105623 · Linear programming and duality
98

## Slide 99
4. When capacity changes, reconnect all four ideas
2105623 · Linear programming and duality
99

## Slide 100
References and optional follow-up
Boyd and Vandenberghe, Convex Optimization: Sections 4.3, 5.2, 5.5, and
5.6.
SciPy documentation: linprog(method="highs"), marginals and residuals.
Optional Python practice: reproduce these examples with
scipy.optimize.linprog.
2105623 · Linear programming and duality
100